 1). Backlight Control
        Using this backlight control feature the user can ' TURN ON ' or ' TURN OFF ' the LCD backlight.

Command:
- bak 1 It switches ON the LCD backlight.
- bak 0 It switches OFF the LCD backlight.

For example:
        If the user sends 'bak 1' command searially using UART to the LCD BackPack , then the LCD backlight turns ON and also the user receives an acknowledgement in the serial monitor as 'Backlight ON' .

        If the user sends 'bak 0' command searially using UART to the LCD BackPack , then the LCD backlight turns OFF and also the user receives an acknowledgement in the serial monitor as 'Backlight OFF' .

2). Block Cursor Blink Control
        Using this control feature the user can ' TURN ON ' or ' TURN OFF ' the blinking block cursor on the LCD display.

Command:
- bli 1 It makes the blinking block cursor to appear on the LCD screen.
- bli 0 It masks the blinking block cursor.

For example:
        If the user sends 'bli 1' command serially using UART to the LCD Backpack , then the blinking block cursor appears on the LCD screen at the current cursor position and also the user gets the acknowledgement in the serial monitor as 'Blink ON'.

        If the user sends 'bli 0' command serially using UART to the LCD Backpack , then the blinking block cursor disappears from the current cursor position and also the user gets the acknowledgement in the serial monitor as 'Blink OFF'.

3). Cursor position selection
        With the help of this control feature the user can set the cursor position anywhere on the LCD screen.

Command:
set_YY_XX

        Where 'YY' is the two digit number which represents the colunms on the LCD screen and 'XX' is also a two digit number which represents the rows of the LCD screen.

        Unfortunately, the LCD module (what we are using right now, 16X2) has only two rows that means 'XX' can take only two values 00 & 01. But there are 16 columns on this LCD module so 'YY' can take values from 00 to 15.

For example:
        If the user sends 'set 05 01' command serially using UART to the LCD Backpack , then the cursor is set at 2nd row 6th column on the LCD screen. Also the user receives an acknowledgement on the serial monitor as ' Cursor position selected'.

Command:
hom
        Whenever the user sends this command serially to the LCD Backpack the cursor position is reset that means the cursor position is set to initial position (0,0) and also the user receives an acknowledgement on the serial monitor as ' Cursor position reset'

4). Writing data onto the LCD screen

        Using this feature the user can print his own data on the LCD screen.

Command:
pri user data

        Here 'pri' represents the command, user data is the data that is to be printed on the LCD screen.

For example:
        If the user sends ' pri ElintLabz ' command serially using UART to the LCD Backpack , then the user data “ElintLabz” is printed on the LCD screen from the current cursor position.
The user also receives an acknowledgement on the serial monitor as ' printed '.

Note:
        1). If ‘NO Line Ending’ option is selected in the serial terminal to send commands then the printing message should terminate with ‘space’.
        2). If ‘Newline’ or ' carriage return ' or ' both NL & CR ' options are selected in the serial terminal to send commands then the printing message need not to terminate with ‘space’.

To print a message like “ Hogst Innovative Solutions” , the user should send the following commands in a sequence.
- pri Hogst
- gap
- pri Innovative
- gap
- pri Solutions

5). Underline type Cursor Control
        Using this control feature the user can ' TURN ON ' or ' TURN OFF ' the underline type of cursor on the LCD display.

Command:
- cur 1 It makes the underline type of cursor to appear on the LCD screen.
- cur 0 It masks the underline type of cursor.

For example:
        If the user sends 'cur 1' command serially using UART to the LCD Backpack , then the underline type of cursor appears on the LCD screen at the current cursor position and also the user receives an acknowledgement in the serial monitor as 'Cursor ON'.

        If the user sends 'cur 0' command serially using UART to the LCD Backpack , then the underline type of cursor disappears from the current cursor position and also the user receives an acknowledgement in the serial monitor as 'Cursor OFF'.

6). Display Control
        Using this display control feature the user can ' TURN ON ' or ' TURN OFF ' the LCD display.

Command:
- dis 1 It switches ON the LCD display.
- dis 0 It switches OFF the LCD display.

For example:
        If the user sends 'dis 1' command serially using UART to the LCD BackPack , then the LCD display turns ON which means that the data on the LCD screen is visible to the user and also the user receives an acknowledgement in the serial monitor as 'Display ON' .

        If the user sends 'dis 0' command serially using UART to the LCD BackPack , then the LCD display turns OFF which means that the data on the LCD screen is not visible to the user and also the user receives an acknowledgement in the serial monitor as 'Backlight OFF' .

7). Clearing the LCD screen
        Using this feature the user can erase the entire data on the LCD screen in one shot.

Command:
clr
        Whenever the user sends this command serially to the LCD Backpack the entire data on the LCD screen is erased and the cursor position is reset that means the cursor position is set to initial position (0,0) and also the user receives an acknowledgement on the serial monitor as ' Screen Cleared '.

8). One character space
        Using this the user can get one character space in his user data.

Command:
gap
        Whenever the user sends this command serially to the LCD Backpack the cursor position is incremented that means the cursor position is set one position ahead from the current position providing one character space and also the user receives an acknowledgement on the serial monitor as ' Space provided'

9). Scrolling
        Using this the user can move the entire data on the screen to the right by one position or to the left by one position.

Command:
- sdp 1 It makes the entire data on the LCD screen to move right by one position.
- sdp 0 It makes the entire data on the LCD screen to move left by one position.

For example:
        If the user sends 'sdp 1' command serially using UART to the LCD Backpack , then the entire data on the LCD screen is shifted to the right by one position and also the user receives an acknowledgement in the serial monitor as 'scroll display right'.

        If the user sends 'sdp 0' command serially using UART to the LCD Backpack , then the entire data on the LCD screen is shifted to the left by one position and also the user receives an acknowledgement in the serial monitor as 'scroll display left'.

10). Baudrate Selection
        Using this feature the user can select the different baudrates for the serial communication.

Command:
- bau 1 It selects the baudrate 4800.
- bau 2 It selects the baudrate 9600.
- bau 3 It selects the baudrate 19200.
- bau 4 It selects the baudrate 38400.
- bau 5 It selects the baudrate 57600.
- bau 6 It selects the baudrate 115200.

For example:
        If the user sends 'bau 3' command serially using UART to the LCD Backpack , then the baudrate 19200 is selected for serial communication and the user receives an acknowledgement in the serial monitor as 'Baudrate selected'.

        If the user sends 'bau 8' command serially using UART to the LCD Backpack , then by default the baudrate 9600 is selected for serial communication and the user receives an acknowledgement in the serial monitor as 'Baudrate selected'.

Note: If the user wants to know which baudrate had been selected earlier, then the user should reset the LCD backpack so that the baudrate will be displayed on the LCD screen.

11). AutoScroll

Using this command the user can make the entire data on the screen to automatically scroll to the right once or to the left once.

Command:
        aut 1 It makes the entire data on the LCD screen to autoscroll right by once.
        aut 0 It makes the entire data on the LCD screen to autoscroll left by once.

For example:
        If the user sends ‘aut 1' command serially using UART to the LCD Backpack , then the entire data on the LCD screen is rotated once to right and also the user receives an acknowledgement in the serial monitor as 'Autoscroll Right'.

        If the user sends ‘aut 0' command serially using UART to the LCD Backpack , then the entire data on the LCD screen is rotated once to left and also the user receives an acknowledgement in the serial monitor as 'Autoscroll Left'.

12). Text Direction
        Using this control feature the user can print the data on the LCD screen from Right to Left or from Left to Right .

Command:
- ltr 1 It makes the text to print from Left to Right direction.
- ltr 0 It makes the text to print from Right to Left direction.

For example:
        If the user sends 'ltr 1' command serially using UART to the LCD Backpack , then the user data starts printing from Left to Right direction on the LCD screen from the next printing command and also the user receives an acknowledgement in the serial monitor as 'Left to Right'.

        If the user sends 'ltr 0' command serially using UART to the LCD Backpack , then the user data starts printing from Right to Left direction on the LCD screen from the next printing command and also the user receives an acknowledgement in the serial monitor as 'Right to Left'.